Dock Lift

Typical Specification:

Manufacturer & Type:  This specification covers a hydraulic dock lift as manufactured by Southworth Products of Portland, Maine.  The lift shall be Southworth Model No. ________.

Capacity:  The lift shall have a lifting capacity of ________ lbs. with a ________ % axle loading capacity over the hinged throw-over plate end and opposite end.  Axle loading capacity over the sides shall be 50%.

Travel:  The lift shall have a vertical travel of 59” from a lowered height of ________”.

Speed:  The lift shall have a nominal rise speed of ________FPM.

Platform:  The platform size shall be ________ X ________ feet with diamond plate deck surface.  Platform will incorporate bevel toeguards on four sides, painted safety yellow.

Hinged Throw-Over Plate:  The platform shall be equipped with a 18” X 60” diamond tread throw-over plate on one end.  The split plate shall have full length hinge.

Handrails:  The platform shall be equipped with 42” high removable steel handrails on two sides with midrail and 4” kick plate.  The rail sockets shall be flush with the platform surface.

Power Unit:  The external hydraulic power unit shall be self-contained and filled with hydraulic oil.  The motor shall be ________HP.

Control:  The lift shall be equipped with a constant pressure “UP/DOWN” weatherproof push button, NEMA 3R, on 20’ Koil Kord to allow operator to control lift while on the machine.  Control voltage shall be 24 volts.

Cylinders:  The lift shall be equipped with single acting cylinders having honed seamless tubing, chrome-plated cylinder rods, a metal wiper/scraper in the rod bearing to exclude harmful contaminants, and vent side of cylinders shall be piped back to power unit.

Hydraulic Oil:  The lift shall be supplied with Texaco Rando HD-32 hydraulic oil, or equivalent.  The hydraulic oil shall be a turbine quality oil with rust and oxidation inhibitors plus anti-wear properties.

Bearings:  All pivot points shall have hardened steel pins which operate in long lasting self-lubricated bearings.

Quality Control:  The lift shall be pretested by seller to 10% over full rated capacity.

Safety:  The lift shall incorporate velocity fuses at cylinders to prevent descent from loss of hydraulic pressure.  The power unit shall incorporate adjustable pressure compensated flow control to maintain uniform lowering speed.